## Slide 1
D.I.R.T.T
Digital Instrument for Remote Terrain Testing
An affordable, autonomous robot that collects and analyzes soil samples across crop fields.

## Slide 2: Team Members
Nolan Brechtel
Project Manager | Navigation Lead
George Utz
Chief Scientist | Power & Charging Lead
Cara Belew
Data Backup & Control Lead
Zachary Morrow
Soil Testing Lead
Rebecca Ueltschey
Drivetrain Lead
Dr. Christopher Hudson
Faculty Advisor

## Slide 3: The Problem
25,000
people die every day from hunger and related causes [1]
$41.5B
projected U.S. agricultural trade deficit, FY2026 [2]
49%
of U.S. crop fields show poor health or nutrient imbalance [3]
Agricultural Research Labs
Need affordable, autonomous sampling to reduce technician hours in the field
Independent Farms
Need reliable soil data without the high cost of existing robots
Field Technician
Need to reduce repetitive, manual sampling work
Who We Help

## Slide 4: Competitive Advantage
How soil gets tested today
Manual sampling
A technician walks the field with a hand probe, and samples are mailed to a lab. Results never reach the farmer in the field.
Commercial sampling robots
Rogo's SmartCore is a converted Bobcat skid-steer with RTK GPS and LiDAR, sold as a service at $3.50–
4.50 per acre [4].
The gap
Accurate, but every survey is a recurring cost. Small farms and labs sample less often than they should.
What D.I.R.T.T does differently
About $1,000 to build
Owned by the farm or lab, with no per-acre service fee.
Answers in the field
pH, EC, temperature and moisture sent back live over LoRa radio.
Runs on sunlight
A 30 W solar panel stretches each survey day.
Small and light
Under 20 kg, so it fits in a pickup bed and stays light on the soil.
Trade-off: a screening tool, not lab-grade. It points farmers to the spots worth a lab test.

## Slide 5: System Diagram
ON THE ROBOT
BASE STATION
Navigation
Nolan Brechtel
•
•
•
SpeedyBee F405 Wing running ArduPilot Rover u-blox M10 GPS + compass on a mast Geofence, e-stop, bump switches, RC override
Data & Control
Cara Belew
•
•
•
Raspberry Pi 3 A+ runs the mission
LoRa Bonnet with OLED status screen Heartbeat, retries, return-home logic
Drivetrain
Rebecca Ueltschey
•
•
•
4× 12 V gearmotors with encoders
Dual-channel motor driver, skid steer
5052 aluminum chassis
Soil Testing
Zachary Morrow
•
•
•
L16 linear actuator, 200 N, position feedback
4-in-1 probe: pH, EC, temp, moisture
Actuator stall = rock strike
Power & Charging
George Utz · feeds every subsystem
•
•
•
30 W solar panel → PWM charge controller
12.8 V LiFePO4 battery, fused branches
12 V → 5 V regulator; plug-in charge port
Base Station
Data & Control · Cara Belew
MAVLink UART
•
915 MHz LoRa link
•
test points · results · heartbeat
•
•
Raspberry Pi 5 with a LoRa Bonnet
Hands out one test point at a time
Watches the robot's heartbeat; sends COME HOME
Laptop shows a live map and saves results to CSV
PWM to motor driver
RS485 · I2C · GPIO
12 V
5 V

## Slide 6: Features
F1 Drives itself
Navigates to GPS test points across a field with no driver.
F2 Tests the soil
Pushes a probe into the ground and stops if it hits a rock.
F3 Four readings per point pH, electrical conductivity (EC), temperature and moisture.
F5 Comes home on its own
If the radio link drops, it pulls the probe and drives back.
F4 Sun-powered
A solar panel tops up the battery; plug in to charge between runs.
F6 A field heat map for the farmer
The base logs each reading with its location for a map view and file export.

## Slide 7: Constraints
C1
≤ $1,000
Total project budget
C2
Apr 2027
Field-ready prototype
C3
Communication
Data must be transmitted wirelessly
C4
Weather Proof
The enclosure must protect the electronics from dust particles larger than 2.5mm and water spraying from a 60-degree angle
C5
Solar Charging
No power out in the field.

## Slide 8: Requirements
ID | Requirement | Target (measurable) | Feature | How we verify it
R1 | Reach each commanded test point | Within 5 m of the target | F1 | GPS log vs. a surveyed marker
R2 | Drive across the field | ≥ 0.5 m/s cruise on grass | F1 | Timed 20 m run
R3 | Climb slopes at full load | 15% grade at 20 kg | F1 | Ramp test
R4 | Stop on e-stop | Motors stopped in ≤ 3 s | F1, F2 | Timed video, 10 trials
R5 | Stay inside the field boundary | 0 geofence breaches in 10 runs | F1 | Simulator + field runs
R6 | Insert, read and retract the probe | Full cycle ≤ 60 s | F2, F3 | Soil-bin test, stopwatch
R7 | Detect a rock strike | Push stops ≤ 3 s after a stall | F2 | Buried-brick test
R8 | Report four soil values | pH ±0.5, temperature ±1 °C vs. reference | F3 | 3 soil samples vs. handheld meter
R9 | Deliver results to the base | ≥ 90% of messages at ≥ 500 m line of sight | F6 | 100-message range test
R10 | Return home when the link drops | Loss detected ≤ 20 s; probe up before moving | F6 | Base radio switched off mid-test
R11 | Survey on one charge | ≥ 1 h of operation with no sun | F4 | Battery run-down test
R12 | Log and map results | 90% of received results saved with GPS + time | F6 | Robot log vs. base CSV

## Slide 9: Standards
FCC 47 CFR Part 15.247
Unlicensed 902–928 MHz radios: our LoRa link stays in band and at ≤ +20 dBm.
IEC 60529 (IP Code)
Ingress protection: IP33 target for the electronics bay; the soil probe is IP68.
ANSI/A3 R15.08-1-2020
Mobile-robot safety: e-stop, protective stop and manual override.
IEC 62133-2
Lithium battery safety: we buy only LiFePO4 packs certified to it.
MAVLink 2
Message protocol between the Raspberry Pi and the ArduPilot flight controller.
Modbus RTU over TIA-485-A
Serial bus and protocol used to read the 4-in-1 soil sensor.
ISO 10390:2021
Reference method for soil pH, used to check our pH readings.
IPC J-STD-001
Workmanship standard for the soldered connections on the robot.

## Slide 10: Component 1: Flight Controller
What it must do
Run ArduPilot Rover: fuse GPS, compass and IMU, drive both skid-steer motor channels, and keep its own failsafes running even if the Pi crashes.
Selection metrics
Cost ≤ $75, to leave budget for solar
Runs ArduPilot Rover (tested navigation and failsafes)
Serial ports for GPS, the Pi (MAVLink)
Battery voltage and current sensing for low-battery return
In stock now
 | Pixhawk 6C Mini | Matek H743-Slim V4 | SpeedyBee F405 Wing
Price | $176.99 | $128.99 | $67.26
Processor · flash | STM32H743 · 2 MB | STM32H743 · 2 MB | STM32F405 · 1 MB
ArduPilot firmware | Standard build | Standard build | Custom build (trimmed)
Wiring | Plug-in JST-GH | Solder pads | Pads + power board
Battery sensing | Extra power module | Onboard | Onboard, 90 A sensor
Meets ≤ $75 | ✗ | ✗ | ✓
Choice: SpeedyBee F405 Wing. It runs the same ArduPilot Rover software for $80–130 less than the alternatives.
Trade-offs: 1 MB of flash means a custom firmware build (Rover, MAVLink, geofence, failsafes), and the wiring is soldered.
Prices: Pyrodrone, team design summary, RaceDayQuads (Oct 2026) [8]

## Slide 11: Component 2: Robot Computer
What it must do
Run the mission on the robot: talk to the base over LoRa, command the flight controller over MAVLink, drive the probe and read the soil sensor.
Selection metrics
Price ≤ $30
In stock now
Low idle power for a solar robot
Runs Raspberry Pi OS, so the LoRa Bonnet and its Python libraries work
USB port for the RS485 sensor adapter
 | Pi Zero 2 W | Pi 3 Model A+ | Pi 5 (1 GB)
Price | $15 (list) | $25 | $45
Availability | Sold out | In stock | In stock
Idle power | 0.4 W | ~1–2 W (est.) | ~3 W
CPU · RAM | 4× A53 1.0 GHz · 512 MB | 4× A53 1.4 GHz · 512 MB | 4× A76 2.4 GHz · 1 GB
Works with Bonnet | ✓ | ✓ | ✓
USB for RS485 | Needs OTG adapter | Full-size USB-A | 4× USB-A
Choice: Raspberry Pi 3 Model A+ on the robot. Same chip family and software as the Zero 2 W, in stock today, and its USB-A port takes the RS485 adapter directly.
Impact: about 1 W more in the power budget than the Zero 2 W. The LoRa Bonnet sits on a stacking header, so the serial, I2C and GPIO pins stay free. Also considered: Orange Pi Zero 2W (no Raspberry Pi OS).

## Slide 12: Component 3: Probe Actuator
 | Actuonix L16 (150:1) | Actuonix P16 (256:1) | Stepper + lead screw
Price | ~$100 | $106.59 | ~$172
Push force | 200 N (250 N static) | 300 N (500 N static) | ~250 N
Speed | 8 mm/s | 2.5–4.8 mm/s | Set by driver
Position feedback | Potentiometer | Potentiometer | None; homing switch
Stall current @ 12 V | 0.65 A | 1.0 A | Draws holding current
Sealing | IP54 | IP54 | Unsealed
What it must do
Push the 4-in-1 soil probe into the ground, hold it while the Pi reads, then pull it out, and tell the Pi when it hits something it can't push through.
Selection metrics
Push force 100–250 N
Insert-and-retract cycle ≤ 60 s
Built-in position feedback
Runs from 12 V at low current
Cost ≤ $125
140 mm stroke takes ~18 s each way, against 31 s or more for the P16) and the lowest current.
Impact: its position feedback lets the Pi detect a stall (a rock), so the load cell and its amplifier were cut. It stands ~8 in above the deck, so the solar panel mount must clear it.

## Slide 13: Gantt Chart: Capstone I

## Slide 14: Capstone I Deliverables
Subsystem / lead | Requirements | Demonstration setup and test method | % Grade | % Earned
Data & Control | Robot Pi and base exchange TEST, OK and RESULT messages over LoRa with ≥ 90% delivery (after retries) at ≥ 500 m line of sight. [8%] Heartbeat detects a dead link within 20 s (3 missed beats of 5 s). [6%] Base logs 100% of received results to CSV with time and GPS position. [6%] | Two Pis with LoRa Bonnets on a campus field 500 m apart send 100 scripted messages; the delivery rate is counted from both logs (data report). Live: the base radio is switched off; the robot's OLED shows LINK LOST and the elapsed time is read from the log. The base CSV is opened on the laptop and checked line by line against the robot's send log. | 20% | 
Soil Testing | Pi reads pH, EC, temperature and moisture over Modbus at least every 5 s. [6%] Readings agree with a handheld reference meter: pH within ±0.5 and temperature within ±1 °C on 3 soil samples. [8%] Actuator pushes the probe into a soil bin and stops within 3 s of stalling on a buried obstruction. [6%] | Live console shows all four values updating from the sensor in a soil sample. Three prepared samples (dry, moist, limed) are measured by our sensor and by the reference meter; a table of differences is provided. Actuator on a 3D-printed test stand over a soil bin; a brick buried 4 cm down triggers the stall stop, timed from the log. | 20% | 
Drivetrain | Chassis fabricated and assembled with all four motors and wheels; mass with ballast ≤ 20 kg. [6%] Under RC control, drives ≥ 0.5 m/s on grass and turns in place. [7%] Climbs a 20% grade with 20 kg on board; ground clearance ≥ 3 in. [7%] | Robot is weighed on a scale with ballast in place. Timed 20 m run on campus grass (3 trials, average speed reported) and a turn-in-place demonstration. Plywood ramp set to a 20% (11.3°) grade with ballast aboard; clearance measured with a tape at the lowest point. | 20% | 
Demo | All 3 subsystems are ready to demo at the time scheduled. Each requirement and corresponding demonstration setups written above have been attempted. |  | 40% | 
Total |  |  | 100% | 

## Slide 15: Future Work
Capstone I · Fall 2026
•
•
•
•
Prove 3 subsystem on the bench
LoRa link, soil readings, flight controller in the simulator
Chassis built and driving
Solar charging on the bench
Capstone II · Spring 2027
•
•
•
•
Integrate everything into one robot
Autonomous multi-point surveys
Link-loss, e-stop and geofence tests
Field trials and final demo
Beyond
•
•
•
•
Automatic docking and charging station
Outrigger legs if lift tests need them
Nutrient (NPK) sensing and a field heat map
Several robots per field

## Slide 16: Broader Impact
Farmers and labs
A ~$1,000 robot puts field-scale soil data within reach of small farms and research labs that can't pay per-acre sampling services.
Environment
Knowing where soil needs help lets farmers apply fertilizer and lime only where it's needed, cutting waste and nutrient runoff.
Food security
Better-managed soil supports better yields, part of feeding a world where hunger still kills thousands every day [1].
Workforce
It automates the repetitive walk-and-probe work, so technicians spend their time on analysis and decisions.

## Slide 17: References
World Food Programme (via Xinhua), “WFP says hunger kills more than AIDS, malaria, tuberculosis combined,” ReliefWeb, Jun. 4, 2009.
R. Hanrahan, “USDA projects ag trade deficit will fall to $41.5 billion in 2026,” Farm Policy News, Univ. of Illinois, Aug. 29, 2025.
Source for the 49% crop-field figure: team to add before presenting.
“Robotic soil sampler is slow but consistent” (Rogo Ag SmartCore), The Western Producer, Jan. 2020.
PiShop.us and Newark, Raspberry Pi 3 Model A+ product pages, accessed Oct. 2026.
raspberry.tips, “Raspberry Pi Zero 2 W sold out: why, for how long, and which alternative,” Sep. 14, 2026; power consumption data, 2026.
M. Larabel, “Raspberry Pi 5 2GB price increases to $77.50 USD,” Phoronix, Oct. 1, 2026.
RaceDayQuads, SpeedyBee F405 WING APP; Pyrodrone, Holybro Pixhawk 6C Mini; ArduPilot, “Firmware limitations on autopilot hardware”; accessed Oct. 2026.
Actuonix L16-140-150-12-P and P16-150-256-12-P specifications, ThingBits and RobotShop, accessed Oct. 2026.

## Slide 18
Questions?
Mid-Semester Design Review
Fall 2026
Digital Instrument for Remote Terrain Testing